SCHOOL BUS PM		Front

| **STEAM OFF ENGINE AND FRONT END ** |
| --- |
| A. GENERAL INSPECTION | OK | NEEDS WORK | B. AROUND VEHICLE INSPECTION | OK | NEEDS WORK |
| 1. ACCELERATOR |  |  | 1. TIRES BRAKE SHOE% TIRE PRESSURE PSI TREADS-32NDS |
| 2. CRANKING MOTOR |  |  |  |
| 3. INSTRUMENTS - Gauges & Warning Lights |  |  |  |
| 4. HEATER & DEFROSTER – Vents, Controls & Functions |  |  |  |
| 5. AIR CONDITIONER – Vents, Controls & Functions |  |  | BRAKE SHOE% TIRE PRESSURE PSI TREADS-32NDS |
| 6. HORNS |  |  |  |
| 7. WIPER BLADES & WASHERS |  |  |  |
| 8. AIR COMPRESSOR OPERATION |  |  |  |
| 9. AIR COMPRESSOR GOVERNOR TEST Cut-off PSI _______ Cut-in PSI _______ |  |  |  |
|  |  |  | 2. WHEELS – Condition, Alignment, Stems & Lug Nuts |  |  |
| 10. LOW AIR PRESSURE WARNING DEVICE |  |  | 3. TIRES – Wear Pattern, Sidewall Condition |  |  |
| 11. CHECK AIR DRYER - Change Every 4 Years |  |  | 4. MUD FLAPS - Splash Guards, Fender Lips |  |  |
| 12. AIR PRESSURE Brakes off DROP Brakes applied |  |  | 5. VEHICLE APPEARANCE |  |  |
|  |  |  | 6. LIGHTS, SIGNALS, REFLECTORS |  |  |
| 13. SEATS - Frames & Cushions |  |  | 7. 8-WAY LIGHTS |  |  |
| 14. PARKING BRAKE – Spring Brake (if equipped) |  |  | 9. BODY MOUNTS |  |  |
| 15. HYDRAULIC BOOSTER & MASTER CYLINDER - Low Pressure Warning Devices |  |  | 10. EXHAUST MOUNTING |  |  |
| 16. MIRRORS – Glass, Controls & Heaters |  |  | 11. FUEL TANK MOUNTING |  |  |
| 17. CHECK LOADING DOOR |  |  |  |  |  |
| 18. DOORS -Lube & Check Operation & Seals |  |  | C. UNDER HOOD INSPECTION |
| 19. WINDOWS -Lube & Check Latches & Operation |  |  | 1. HOOD – Mounts, Hold Down Latches, Operation |  |  |
| 20. WINDSHIELD -Check Condition & Seals |  |  | 2. RADIATOR CORE – Dirt & Obstructions |  |  |
| 21. EMERGENCY BUZZERS & LATCHES - Windows, Hatch, Door |  |  | 3. RADIATOR MOUNTING & SHROUD |  |  |
| 22. ENGINE FAULT CODES - READ & RECORD |  |  | 4. FAN ASSEMBLY – Hub, Lube, Automatic Operation |  |  |
| 23. HEATER & AC FILTERS - Clean & Inspect |  |  | 5. RADIATOR – Leakage |  |  |
| 24. SAFETY EQUIPMENT – Driver’s Seatbelt, Drag Blanket, Safety & Wheelchair Belts |  |  | 6. COOLANT – Freeze Point |  |  |
| 25. FIRE EXTINGUSHER & TRIANGLES - Tag, Bracket & Mounting |  |  | 7. COOLANT SIGHT GLASS – Clean & Inspect |  |  |
| 26. FIRST AID KIT |  |  | 8. HOSE CONDITION |  |  |
| 27. BODY FLUID KIT |  |  | 9. COOLING SYSTEM - Pressure test & inspect cap |  |  |
|  |  |  | 10. SCA PROTECTION LEVEL |  |  |

BUS NO: _______   DATE: ________ MILEAGE: ________ TECH:______

Back

SCHOOL BUS PM

BUS NO: _______   DATE: ________ MILEAGE: _____

| C. UNDER HOOD INSPECTION (CONT’D) | OK | NEEDS WORK | D. UNDER VEHICLE INSPECTION & LUBRICATION (CONT’D) | OK | NEEDS WORK |
| --- | --- | --- | --- | --- | --- |
| 11. BELTS & TENSIONERS |  |  | 17. BRAKE CHAMBERS |  |  |
| 12. COMPRESSOR(S) - Mounting |  |  | 18. KING PINS – Raise Front End |  |  |
| 13. VIBRATION DAMPER |  |  | 19. FRONT WHEEL BEARINGS |  |  |
| 14. LINES & HOSES – Leaks & Chaffing |  |  | 20. REAR WHEELS |  |  |
| 15. WIRING – Chaffing & Loomed |  |  | 21. BRAKE HOSE – Cracks, Chaffing |  |  |
| 16. AIR INTAKE PIPES |  |  | 22. BRAKE DRUMS – Condition |  |  |
| 17. EXHAUST LEAKS |  |  | 23. FLUID LUBRICATION LEVELS |  |  |
| 18. BATTERIES - Inspect & Clean |  |  | Engine |  |  |
| 19. BATTERIES LOAD TEST - Replace Every 4 Years |  |  | Transmission |  |  |
| 20. BATTERY TERMINALS & CABLES - Inspect & Clean |  |  | Power Steering |  |  |
| 21. BATTERY HOLD DOWN(S) & BOX |  |  | Windshield Washer Solvent |  |  |
| 22. STARTER – Starter Amp Draw ___V |  |  | Coolant |  |  |
| 23. ALTERNATOR – Output Test |  |  | Differential |  |  |
| 24. ADJUST VALVES [Every 4 years or 100,000] |  |  | Wheels / Hubs |  |  |
| D. UNDER VEHICLE INSPECTION/LUBRICATION | E. TEST DRIVE INSPECTION |
| 1. LUBRICATE CHASSIS – PURGE all grease fittings |  |  | 1. STEERING FEEL |  |  |
| 2. FLUID LEAKS – Engine, Transmission, Steering, Differential, Axles. |  |  | 2. SHIFTING EASE |  |  |
| 3. CHANGE ENGINE OIL & FILTER |  |  | 3. BRAKE FEEL - Pulling & Stopping Distance |  |  |
| 4. CHANGE TRANSMISSION FLUID & FILTER |  |  | 4. ABS OPERATION – (If equipped) |  |  |
| 5. CHANGE POWER STEERING FLUID & FILTER |  |  | 5. ENGINE OPERATION – Surging, missing |  |  |
| 6. CHANGE AIR FILTER(S) - Write Date On Filter |  |  | 6. UNUSUAL NOISES – Rattles , Vibrations, Leaks |  |  |
| 7. CHANGE FUEL FILTER(S) |  |  | 7. INTERIOR – Cleanliness |  |  |
| 8. CHANGE CRANKCASE FILTER - 2 Yrs or 30, 000 Miles |  |  | 8. TWO WAY RADIO CHECK |  |  |
| 9. ENGINE & TRANSMISSION MOUNTS |  |  | 9. DVR - Check for Red & Green Light on DVR |  |  |
| 10. DRIVELINES - U-Joints, Yokes, Hanger Brackets, Center Bearings & X-Members. |  |  | 10. INSPECTION STICKER - Install or Update |  |  |
| 11. STEERING SYSTEM – Tie Rods, C-Link, Pitman Arm, Shaft, Joints |  |  |  |  |  |
| 12. SPRINGS, SHOCKS, U-BOLTS, SHACKLES |  |  |  |  |  |
| 13. TRANSMISSION & AXLE PINION FLANGES |  |  |  |  |  |
| 14. AXLE BREATHERS – Clean |  |  |  |  |  |
| 15. AIR TANKS - Check Valves, Drain Moisture |  |  |  |  |  |
| 16. WIRING – Connectors |  |  |  |  |  |